## Slide 1
SATELLITE INTERNET COMMUNICATION
Using OSI Layers
TECHNICAL PRESENTATION
Presented By:
R.SriVidya
192472261

## Slide 2
Satellite Internet: System Overview
User Terminal VSAT dish / modem converts user data into RF signals for uplink.
Satellite (GEO / MEO / LEO) Receives, amplifies, and relays signals — acts as a relay node, not an IP router in most designs.
Ground Station / Gateway Bridges the satellite RF link to terrestrial fiber and the public Internet.
OSI Model as a Framework Each layer solves a distinct problem: signal transport, framing, routing, and reliable delivery over a long, lossy path.
User Terminal
Satellite Relay
Ground Gateway
Internet Backbone

## Slide 3
Layers 1–2: Physical & Data Link
Getting bits reliably across the space segment
Physical Layer
RF transmission in Ku, Ka, or C bands
Modulation: QPSK, 8PSK, 16-APSK
Free-space path loss & rain fade handled here
Defines power, frequency, and antenna geometry
Data Link Layer
Framing via DVB-S2 / DVB-RCS standards
Forward Error Correction (FEC) for high bit-error rates
MAC scheduling: TDMA shares uplink capacity
ARQ retransmission for corrupted frames

## Slide 4
Layers 3–4: Network & Transport
Routing packets — and fighting the physics of latency
Network Layer
IP addressing & packet routing across gateways
GEO satellites usually act as bent-pipe relays; LEO constellations increasingly route on-board
Inter-satellite links (ISLs) enable mesh routing in modern constellations
Handles mobility as LEO satellites move relative to ground stations
Transport Layer
~500–600 ms round-trip time for GEO links stresses standard TCP.
Large bandwidth-delay product needs bigger TCP windows
Performance Enhancing Proxies (PEPs) split connections
Satellite-tuned variants (TCP Hybla, Peach+) improve throughput

## Slide 5
Layers 5–7: Session, Presentation & Application
Where the user's traffic actually lives
Session Layer
Manages and re-establishes sessions after link outages caused by rain fade, handoffs, or brief signal loss.
Presentation Layer
TLS/SSL encryption and data compression reduce payload size — critical given constrained satellite bandwidth.
Application Layer
HTTP/HTTPS, DNS, VoIP, and video streaming — often optimized with caching and content pre-fetching at the gateway.

## Slide 6
Challenges & Future Trends
Where satellite Internet architecture is heading
600ms
GEO round-trip
latency
25ms
Typical LEO
(Starlink-class) latency
1000+
Satellites in a modern
LEO mesh constellation
LEO constellations (Starlink, OneWeb, Kuiper) cut latency dramatically and enable on-board routing via laser inter-satellite links.
Edge computing at gateways and next-gen protocols (QUIC, HTTP/3) further reduce the impact of propagation delay on user experience.
Conclusion: The OSI model remains the essential lens for isolating and solving each engineering challenge — from RF physics to application-level QoE — in satellite-delivered Internet.